## Slide 1
Current State
Motor instruction Byte: 000x xxxx
Battery
Left sensor
Right sensor
Side sensor
Grabber Motor (R)
Grabber Motor (L)
Wheel Motor (L)
Wheel Motor (R)
IR Sensor
Red LED
Green LED
Laptop
(python)
Phone Hotspot
Camera 3
0th Bit (least significant):
1 - Reverse Right Motor
0 - Forward Right Motor
1st Bit:
1 - Right Motor on
0 - Right Motor off
2nd Bit:
1 - Reverse Left Motor
0 - Forward Left Motor
3rd Bit:
1 - Left Motor on
0 - Left Motor off
4th Bit:
1 – Goto grabbing sequence
0 – Continue as usual
State:
0 – Initial line following
1 – Nav to target
2 – Grab target
3 – Nav to T junction
4 – Line follow & dump
5 – Return to T junc through tunnel w/ line following
6 – Return to start pos.
7 – Do nothing (end)
A2
A1
A0
Live video feed
(USB port)
Arduino
4
3
1
2
Power line
Pulse counter circuit
Power line
System and Comms Diagram

## Slide 2
motor_L()
motor_R()
rotate()
forward()
follow_line()
msg_motor()
grabber_L()
grabber_R()
dump()
grab()
Update motor
Basic actions
Complex actions
Main Code
Code Structure